## Slide 1: Competition Bridge Tester
Carter Mealey
Ben Holleran

## Slide 2: Preliminary Specs
1 meter Span – Troitsky Competition
5 Tons – Current Record 3.2 Tons
Movable by Two People
Displays Load on Large Display
Accurate to 1% Load
Precise to 1 lb During competition
8” Active Distance

## Slide 3: Preliminary Calculations
1020 Cold Rolled Mild Steel – Easily Welded
  43.5 KSI Yield
  = Max Elastic Force
  2” Square Tubing 1/16” Wall = .484 in2 = 10.5 Tons
  2” Square Tubing 1/8” Wall = .9375 in2 = 20.4 Tons
5 Tons
  = = 10 in2
  A = πr2 = r = = 1.78 in = 3.6” Piston

## Slide 4: Brainstorming
Screen Content
  Current Load
  Max Load
  Stress Over Strain Curve
Display Methods
  Computer Monitor
  7 Segment LED display
  LED Matrix Display
  Web Page
Piston
  Pneumatic
  Hydraulic
Force Measurement
  Load Cell
  Pressure Sensor
Embedded Processor
  Arduino
  Computer
  Raspberry Pi

## Slide 5: Technology We Will Need to Research
Raspberry Pi
7 Segment Drivers
Hydraulic Systems
Welding

## Slide 6: Communication
Emailed Gordon Reynolds, John Diebold
  No Reply
  Some “Lunch Room” Conversations
    Result was to look at the Troitsky Competition

## Slide 7: Research Results
Strain Gauges and Pressure Sensors are ~$500
  Large Scale Force Measurement is Done by Measuring Pressure in Precision Cylinder
Troitsky Competition
  Current Record Holder is 3.2 Tons.
    McMaster University
  Span is 1 Meter

## Slide 8: System Diagram
Lower Truss
Upper Truss
Rasberry Pi
Piston
Support
Support
7 Segment Display
Hydrolic Pump
Force Guage
Monitor
Wheels