## Slide 1: Competition Bridge Tester
Carter Mealey
Ben Holleran
Notes: General introduction type stuff.

## Slide 2: What We Will Discuss
The background of the course and project
Our solution
System diagrams
Areas of responsibility
Rough Timeline
Rough Budget

## Slide 3: Course Background
Student design project
  Vermont Technical College senior projects
    Select project from list provided
    Communicate with client to determine specs
    Create design to meet specs
    Review design with client and project managers
      Create new specs and adjust design direction
    Revise design to reflect changes
    Build design while working with client
    Final presentation
Notes: The course that we are part
Let me tell you a little bit about the

## Slide 4: Project Background
Selected project: Bridge Tester
  Design and build testing equipment compatible with Trotski Competition
  Design project to be open source
Budget | $7000
Client | John Diebold, Gordon Reynolds

## Slide 5: Preliminary Specs
1 meter Span – Trotski Competition
5 Tons – Current Record 3.2 Tons
Movable by Two People
Displays Load on Large Display
Accurate to 1% Load
Precise to 1 lb During competition
8” Piston Throw

## Slide 6: Preliminary Calculations
1020 Cold Rolled Mild Steel – Easily Welded
  43.5 KSI Yield
  = Max Elastic Force
  2” Square Tubing 1/16” Wall = .484 in2 = 10.5 Tons
  2” Square Tubing 1/8” Wall = .9375 in2 = 20.4 Tons
5 Tons
  = = 10 in2
  A = πr2 = r = = 1.78 in = 3.6⌀” Piston

## Slide 7: Preliminary Design
Hydraulic Cylinder
Truss instead of I-Beam to save weight
3” LED 7 segment display for load
Raspberry Pi as controller
  HDMI monitor for force over deflection readout
  Web interface to download logs.

## Slide 8
8888
Control box:
Raspberry Pi
I2C A2D
Switches
GPIO Interface
HDMI Cord
LCD Screen
Large 7-Segment Display
Hydraulic
Cylinder
Pressure
Line
Hydraulic Pump
2in x 2in Hollow
Steel Tubing Frame
Bridge Goes Here

## Slide 9: Areas of Responsibility
 | Ben | Carter
Mechanical | Hydraulics | Frame
Electrical | Raspberry Pi & Controls | 7-Segment Display
Software | I2C Interfaces | Graphical Interfaces

## Slide 10: Rough Timeline

## Slide 11: Rough Budget

## Slide 12
8888
Control box:
Raspberry Pi
I2C A2D
Switches
GPIO Interface
HDMI Cord
LCD Screen
Large 7-Segment Display
Hydraulic
Cylinder
Pressure
Line
Hydraulic Pump
2in x 2in Hollow
Steel Tubing Frame
Bridge Goes Here