## Slide 1: Competition Bridge Tester
Carter Mealey
Ben Holleran
Notes: General introduction type stuff.

## Slide 2: What We Will Discuss
The background of the course and project
Our solution
System diagrams
Areas of responsibility
Rough Timeline
Rough Budget
Notes: We will discuss the background of our project and the course goals. We will also go over our solution to the selected project and show our system diagram. Areas of responsibility will be reviewed as well as a preliminary timeline and rough budget.

## Slide 3: Course Background
Student design project
  Vermont Technical College senior projects
    Select project from list provided
    Communicate with client to determine specs
    Create design to meet specs
    Review design with client and project managers
      Create new specs and adjust design direction
    Revise design to reflect changes
    Build design while working with client
    Final presentation
Notes: This course is a year long course spread over the two senior semesters. We were tasked with picking a project from a list. For our projects we must communicate with our clients and create a design that fulfills the design requirements. As the project progresses and matures, meetings with the clients will continue to show progress and address concerns. The design will be revised to reflect the changes that the client requests. At the end of April the projects will be demonstrated and presented.

## Slide 4: Project Background
Selected project: Bridge Tester
  Design and build testing equipment compatible with Trotski Competition
  Design project to be open source
Budget | $7000
Clients | John Diebold Gordon Reynolds
Notes: Our project is to build a bridge tester that is compatible with the Troitski Bridge Competition in April. Our clients are John Diebold and Gordon Reynolds who are both Architecture professors at VTC. We were given a design budget of around $7000 to work with. We added an extra specification to our project that it should be open source so other schools can make their own based on our design.

## Slide 5: Preliminary Specs
1 meter Span – Troitski Competition
5 Tons – Current Record 3.2 Tons
Movable by Two People
Displays Load on Large Display
Accurate to 1% Load
Precise to 1 lb During competition
14” Piston Throw
Notes: We are basing our design off the tester used at the Troitski competition in Montreal. We hope to make a tester that will allow the students here at VTC to practice by testing bridges here before going up to Montreal. We also hope that by making the tester available here at VTC, we can hold competitions for the local high schools and potentially colleges in the region.
We have worked out some of the preliminary specs with the architecture professors:
The tester will have the ability to test a bridge with a 1 meter span.
The current record at the Troitski competition is only 3.2 tons, so we will make our tester strong enough to break a bridge with 5 tons.
One of the things that we noticed while looking at the current Troitski tester is that it is very heavy and hard to move around. We will be designing our tester so it can be moved into Judd gym by two people. This means it needs to be able to be carried down stairs and fit through a single standard door.
We will be trying to make the tester accurate to within 1%. This means that the displayed load will be within 1% of the true force applied to the bridge
We will also try to ensure that the Displayed load will be precise to within 1 lb, the smallest unit we will be measuring, between competitions. This will ensure that a bridge breaking at 501lb really did take more force than the bridge that broke at 500lb earlier that afternoon.
The tester will have a 14” throw enabling the competition to “serve” bridges of different heights

## Slide 6: Preliminary Calculations
1020 Cold Rolled Mild Steel – Easily Welded
  43.5 KSI Yield
  = Max Elastic Force
  2” Square Tubing 1/16” Wall = .484 in2 = 10.5 Tons
  2” Square Tubing 1/8” Wall = .9375 in2 = 20.4 Tons
5 Tons
  = = 10 in2
  A = πr2 = r = = 1.78 in = 3.6⌀” Piston
Notes: In this slide you will see some preliminary calculations to check the viability of the project. I wanted to see how much steel would be needed to hold the kind of forces that we will be seeing in this tester. I picked 1020 cold rolled steel as it is a common steel for framing, and is easily weldable.
Before I get into the calculations, let me explain a few terms first. The yield strength of a material is the “pressure” that needs to be applied to an area before it permanently deforms. For 1020 cold rolled, this means that a 1” square bar can have 20 tons hung on it without it permanently stretching.
This means that 2” square tubing with 1/16” walls, which has about .5 square inches of material, can hold about 10 tons. If the wall thickness was expanded to ⅛” then the max load is about 20 tons.
The other area of concern is the piston size. To calculate the size, I started with the premise that 1000PSI was the max PSI that should be ruin through the hydraulic lines, and that meant that a 5 ton piston would have a diameter of 3.6”
From these calculations it is clear that it will be possible to build a tester that uses a hydraulic cylinder, and steel tube framing.

## Slide 7: Preliminary Design
Hydraulic Cylinder
Truss instead of I-Beam to save weight
3” LED 7 segment display for load
Raspberry Pi as controller
  Power of a computer
  Individually controlled pins like a microcontroller
  HDMI monitor for force over deflection readout
  Web interface to download logs.
Notes: Our preliminary design consists of a hydraulic cylinder fixed to the top of a truss frame design. The frame must fit a bridge with a span of a meter within it. The hydraulic cylinder has a stroke of 14” which should allow for plenty of reach. We are using a steel truss design over an I-Beam design in order to save overall weight while maintaining high structural strength and rigidity. A 7-Segment with 3” tall characters will be used to allow the audience to clearly see the current load value from a distance. A Raspberry Pi microcomputer will be used as the main controller for our project. It has the power of a standard computer with the low price and super small size of a microcontroller. An LCD screen with a custom GUI showing deformation in live time will be connected directly to the Raspberry Pi using an HDMI cable. A web interface will also be designed to allow for the downloading of run logs from remote locations.

## Slide 8
8888
Control box:
Raspberry Pi
I2C A2D
Switches
GPIO Interface
HDMI Cord
LCD Screen
Large 7-Segment Display
Hydraulic
Cylinder
Pressure
Line
Hydraulic Pump
2in x 2in Hollow
Steel Tubing Frame
Bridge Goes Here
Notes: Our design consists of a steel frame with trusses made from 2in square tubing. This allows for great strength while maintaining relatively low weight. There is a hydraulic cylinder with a large throw of around 14”. The cylinder is pressurized with a large hydraulic pump powered by an electric motor. There is a control box on the side of the frame for the operator to control the tester. There is a Raspberry Pi inside control box that controls 7-Segment display, the LCD screen, hydraulic pump, and reads the pressure gauge using various interface methods all translated over the GPIO pins. The frame is on wheels for easy mobility.

## Slide 9: Areas of Responsibility
 | Ben | Carter
Mechanical | Hydraulics | Frame
Electrical | Raspberry Pi & Controls | 7-Segment Display
Software | I2C Sensors Interface | Graphical Interface
Notes: The project is broken up into multiple parts. The Hydraulics, Raspberry Pi and I2C will primarily be done by Ben.
The Frame, 7-Segment Display and Graphical Interface will be handled primarily by Carter.

## Slide 10: Preliminary Timeline
Week | 1/13/2014 | 1/20/2014 | 1/27/2014 | 2/3/2014 | 2/10/2014 | 2/17/2014 | 2/24/2014 | 3/3/2014 | 3/10/2014 | 3/17/2014 | 3/24/2014 | 3/31/2014 | 4/7/2014 | 4/14/2014 | 4/21/2014 | 4/28/2014 | 5/5/2014
Hydraulics |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Spec parts | x | x |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Purchase | x | x | x | x |  |  |  |  |  |  |  |  |  |  |  |  | 
Assemble |  |  | x | x | x | x | x | x |  |  |  |  |  |  |  |  | 
Attach to frame |  |  |  |  |  |  | x | x | x |  |  |  |  |  |  |  | 
Calibrate |  |  |  |  |  |  |  |  |  | x |  |  |  |  | x | x | 
Frame |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Design | x | x |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Purchase |  | x | x | x |  |  |  |  |  |  |  |  |  |  |  |  | 
Fabricate |  |  |  | x | x | x | x |  |  |  |  |  |  |  |  |  | 
Assemble |  |  |  |  |  | x | x | x | x |  |  |  |  |  |  |  | 
Raspberry Pi |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Purchase | x |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Install Raspbian OS |  | x |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Program with Python |  |  | x | x | x | x |  |  |  |  |  |  |  |  |  |  | 
Interface |  |  |  | x | x | x | x | x | x | x |  |  |  |  |  |  | 
Attach to Frame |  |  |  |  |  |  |  |  |  |  | x | x | x | x |  |  | 
Notes: Our rough timeline is only for general reference at this point. Things will almost certainly be done earlier or later than specified when planned this far ahead of time. Our schedule has us ordering parts the first week of the semester. Things will be assembled and programmed in the following weeks. As the deadline approaches the project will be assembled together and calibrated.

## Slide 11: Preliminary Budget
Name | Link | Qt | Price | Total | 
Electronics |  |  |  |  | $ 394.99
7 segment display |  | 10 | $ 2.50 | $ 24.99 | 
Rasberry Pi |  | 1 | $ 50.00 | $ 50.00 | 
Monitor |  | 1 | $ 100.00 | $ 100.00 | 
hdmi cord |  | 1 | $ 20.00 | $ 20.00 | 
i2c ADC |  | 5 | $ 4.00 | $ 20.00 | 
Switches |  | 6 | $ 5.00 | $ 30.00 | 
Misc |  | 1 | $ 150.00 | $ 150.00 | 
 |  |  |  | $ - | 
 |  |  |  | $ - | 
Hydrolics |  |  |  |  | $ 1,028.00
Pump |  | 1 | $ 100.00 | $ 100.00 | 
Motor |  | 1 | $ 100.00 | $ 100.00 | 
Cylinder |  | 1 | $ 236.50 | $ 236.50 | 
Sensor |  | 1 | $391.50 | $ 391.50 | 
Lines |  | 2 | $ 100.00 | $ 200.00 | 
 |  |  |  | $ - | 
Mechanical |  |  |  |  | $ 340.00
Castors |  | 4 | $ 10.00 | $ 40.00 | 
Misc Hardware |  | 1 | $ 300.00 | $ 300.00 | 
 |  |  |  | $ - | 
Raw Materials |  |  |  |  | $ 498.00
Frame Steel |  | 10 | $ 42.00 | $ 420.00 | 
Paint |  | 4 | $ 7.00 | $ 28.00 | 
Aluminum plate |  | 1 | $ 50.00 | $ 50.00 | 
Category | Total
Electronics | $ 394.99
Hydrolics | $ 1,028.00
Mechanical | $ 340.00
Raw Materials | $ 498.00
Total | $ 2,260.99
Chart: 
| Electronics | Hydrolics | Mechanical | Raw Materials
Total | 394.99 | 1028 | 340 | 498
Notes: We were given a budget of around $7000. At this point in time we have done some general speccing and estimated some costs for unexpected and unspecified bits of hardware. At the moment our electronics total comes up to around $400, the hydraulics to about $1000, the mechanical to around $350, and the raw materials to around $500. This brings our total to just under $2300 which is significantly under budget. We are sure there will be unexpected costs to increase the total project costs but we will still come in quite a bit under budget.

## Slide 12: Conclusion
In Conclusion:
  Design meets Course specs
  Design meets Client specs
  Design is constructible within timeframe
  Design is within budget
Notes: Our project fulfills all of the requirements for the class. It has the required amount of mechanical, electrical, and software specifications. Our design fulfills the specifications of Mr. Diebolds the client. Our project will be able to be constructed in a timely fashion and will fall within our budget constraints.

## Slide 13: Questions?