## Slide 1: Bridge Tester ELM-4702 Projects II
Ben Holleran
Carter Mealey

## Slide 2: What We Will Discuss
Course Outline
Our Selected Project
Project Background
Design Constraints
  Troitsky Competition and Specifications
Our Design Solution
  Project Management
  Subsystems designs
  Technical Details
Conclusion

## Slide 3: Course Outline
Design and build a project that satisfies customer’s project restrictions
Document engineering process throughout whole project
Exercise proper engineering techniques
Follow project throughout entire development lifecycle
Present project to peers and deliver to customer

## Slide 4: Selected Project
Popsicle stick bridge crusher
Deliver to the VTC Civil Engineering departement
Meet all Troitsky Bridge Competition specifications

## Slide 5: Project Purpose
To prepare VTC students for the annual Concordia University Troitsky Competition
Teach local High Schools about engineering and encourge them to persue STEM degrees

## Slide 6: Project Sponsors
VTC Civil Engineering departement
Clients | John Diebold Gordon Reynolds
Budget | $3500

## Slide 7: Design Specifications
1 meter span
10 Tons
Mobile enough to move between buildings
Load display visible across Judd Gym
Accurate to 1% Load
Precise to 1% between bridges
14” Piston Throw – Allows different height bridges to be tested
100mm x 200mm Crush plate as per competition specifications

## Slide 8: Troitsky Competition
Concordia University
Colleges compete to build the strongest bridge
Strongest bridge was made by MIT and held over six tons
Load display
(enlarged)
Piston and piston extender

## Slide 9: Troitsky Competition History
Started in 1984
1991 first US team
1994, crusher exploded.
  Mark on ceiling, Oil everywhere.
New crusher, max 6000lb
2000 new crusher. Hydraulic jack
2010 new crusher. Hydraulic jack

## Slide 10: Final Design
Hydraulic cylinder and pump
AC electric motor
Truss instead of I-Beam to save weight
Raspberry Pi microcomputer as controller
  I²C interface
    Deflection data
    Load data
HDMI monitor for load display and force over deflection readout

## Slide 11: Project Management
Project to be Open Source
Github selected for project management
  Version control
  File management
  Task tracking
  Time management

## Slide 12: Work Breakdown Gaant Chart
Put Gaant chart screen shot here
Carter Ben
Project managed via GitHub

## Slide 13: Final Budget
Chart: 
| Electronics | Hydraulics | Mechanical | Raw Materials
Total | 600.95 | 1676.16 | 491.52 | 565.434
Category | Total
Electronics | $ 600.95
Hydraulics | $ 1,676.16
Mechanical | $ 491.52
Raw Materials | $ 565.43
Total | $ 3,334.06
Name | Qt | Price | Shipping | Total | 
Electronics |  |  |  |  | $ 600.95
7 segment display | 5 | $ 16.46 | $ 15.00 | $ 97.30 | 
Rasberry Pi | 1 | $ 55.00 | $ 12.72 | $ 67.72 | 
Monitor | 1 | $ 136.00 | $ - | $ 136.00 | 
hdmi cord | 1 | $ 5.79 | $ - | $ 5.79 | 
i2c ADC | 1 | $ 14.95 | $ 4.07 | $ 19.02 | 
Switches | 1 | $ 5.95 | $ - | $ 5.95 | 
Misc | 1 | $ 150.00 | $ - | $ 150.00 | 
Darlington Array | 6 | $ 2.00 | $ 4.43 | $ 16.43 | 
USB external HDD | 1 | $ 28.00 | $ 7.49 | $ 35.49 | 
7-Seg I2C | 5 | $ 5.95 | $ 7.50 | $ 37.25 | 
Wireless router | 1 | $ 30.00 | $ - | $ 30.00 | 
 |  |  |  | $ - | 
Hydraulics |  |  |  |  | $ 1,676.16
Pump | 1 | $ 171.75 | $ 24.32 | $ 196.07 | 
Motor | 1 | $ 123.00 | $ - | $ 123.00 | 
Cylinder | 1 | $ 236.50 | $ - | $ 236.50 | 
Sensor (0-5V) | 1 | $391.50 | $ - | $ 391.50 | 
Lines | 5 | $ 100.00 | $ - | $ 500.00 | 
Valve | 1 | $ 85.00 | $ - | $ 85.00 | 
Tank | 1 | $ 70.00 | $ - | $ 70.00 | 
Filter housing | 1 | $ 40.00 | $ - | $ 40.00 | 
Filter Cartridge | 1 | $ 20.00 | $ - | $ 20.00 | 
 |  |  | $ - | $ - | 
Motor Coupling | 1 | $ 4.22 | $ - | $ 4.22 | 
Pump Coupling | 1 | $ 5.29 | $ - | $ 5.29 | 
Coupling Spider | 2 | $ 2.29 | $ - | $ 4.58 | 
 |  |  | $ - | $ - | 
 |  |  |  | $ - | 
Mechanical |  |  |  |  | $ 491.52
Castors | 4 | $ 47.88 | $ - | $ 191.52 | 
Misc Hardware | 1 | $ 300.00 | $ - | $ 300.00 | 
 |  |  | $ - | $ - | 
 |  |  | $ - | $ - | 
 |  |  | $ - | $ - | 
 |  |  | $ - | $ - | 
 |  |  | $ - | $ - | 
 |  |  | $ - | $ - | 
 |  |  | $ - | $ - | 
Raw Materials |  |  |  |  | $ 315.21
Frame Steel | 0 | $ - | $ - | $ - | 
0 | .00 ft | $ 2.33 | $ - | $ - | 
0 | .00 ft | $ 3.63 | $ - | $ - | 
0 | .00 ft | $ 12.06 | $ - | $ - | 
Steel Cuts at Capitol | 6 | $ 10.00 | $ - | $ 60.00 | 
 |  | $ - | $ - | $ - | 
 |  | $ - | $ - | $ - | 
Paint | 10 | $ 7.00 | $ - | $ 70.00 | 
Aluminum plate 1'x6'x.5" | 1 | $ 185.21 | $ - | $ 185.21 | 

## Slide 14
Control box:
Raspberry Pi
I2C A2D
  Force
  Deflection
Switches
Hydraulic Handle
Hydraulic
Cylinder
Pressure
Graph
Hydraulic Pump, Motor
3in x 3in Hollow
Steel
Bridge Goes Here
Large Castors
LCD Screen
System Diagram
Hydraulic Resevoir

## Slide 15: The Frame
Notes: The frame is the structure that everything else is built on with this project. The above frame on the left shows the structure under maximum load with very exaggerated displacement visuals. There are a few more beams to be added to the frame but we are waiting on other key parts to fabricate mounting requirements after measurements.

## Slide 16: The Frame
Minimum Safety Factor of 4
Truss Is lighter and stiffer than I beam
Notes: The frame is the structure that everything else is built on with this project. The above frame on the left shows the structure under maximum load with very exaggerated displacement visuals. There are a few more beams to be added to the frame but we are waiting on other key parts to fabricate mounting requirements after measurements.

## Slide 17: Motor to Hydraulic Pump Adapter

## Slide 18: Motor Adaptor Plate

## Slide 19: Hydraulic Subsystem
½ NPT
Pressure Sensor
¼ NPT
¾ NPT
1 ½ NPT
¾-16
Valve has built in pressure relief
Notes: Our hydraulic system has is manually operated and has active extend and retract states. It is capable of outputting between 2K-3Ksi of pressure. It has a return tank and a gear pump with a manual handle.

## Slide 20: Electrical Subsystem Diagram
Raspberry Pi
Monitor
HDD
Control Box
HDMI
USB
I²C
ADC
ADC
Distance Sensor
Pressure Sensor

## Slide 21: Electrical Schematic

## Slide 22: Software Overview
Software to be written in Python
  Easy
  Preexisting libraries
  Interpreted (No compiling needed)
  Integrated thread control
PyGame to draw to screen
  Preinstalled on Pi

## Slide 23: Software Diagram
Input Thread
Reads pressure sensor at 100Hz Reads distance at 10Hz Stores in list
Main Thread
Averages every 10 pressure readings
Draws to graph
Handles button presses
I²C
Sensor readings
List

## Slide 24: Conclusion
In Conclusion:
  Design meets Client specs
  Design is constructible within timeframe
  Design is within budget

## Slide 25: Questions?