## Slide 1: Bridge Tester ELM-4702 Projects II
Ben Holleran
Carter Mealey

## Slide 2: What We Will Discuss
The background of the project
Our solution
System diagrams
Areas of responsibility
Estimated Timeline
Budget
Conclusion

## Slide 3: Project Background
Design and build testing equipment compatible with Trotski Competition
Design project to be open source
Budget | $3500
Clients | John Diebold Gordon Reynolds

## Slide 4: Troitsky Competition
Concordia University
Colleges compete to build the strongest bridge
Strongest bridge was made by MIT and held over six tons
Load display
Piston and piston extender
Crushed Bridge

## Slide 5: Troitsky Competition
Started in 1984
1991 first US team
1994, crusher exploded.
  Mark on ceiling, Oil everywhere.
New crusher, max 6000lb
2000 new crusher. Hydraulic jack
2010 new crusher. Hydraulic jack

## Slide 6: Design Specifications
1 meter span
10 Tons
Mobile enough to move between buildings
Load display visible across Judd Gym
Accurate to 1% Load
Precise to 1% between bridges
14” Piston Throw – Allows different height bridges to be tested

## Slide 7: Final Design
Hydraulic Cylinder
Truss instead of I-Beam to save weight
Raspberry Pi as controller
  HDMI monitor for force over deflection readout
  I²C interface
    4” LED 7 segment display for load
    Deflection data
    Load data

## Slide 8
Control box:
Raspberry Pi
I2C A2D
  Force
  Deflection
Switches
LCD Screen
Large 7-Segment Display
3in x 3in Hollow
Steel Tubing Frame
Bridge Goes Here
Large Castors
System
Diagram
88888
Hydraulic System

## Slide 9: Hydraulic Subsystem
½ NPT
Pressure Sensor
¼ NPT
¾ NPT
1 ½ NPT
¾-16
Valve has built in pressure relief
Notes: Our hydraulic system has is manually operated and has active extend and retract states. It is capable of outputting between 2K-3Ksi of pressure. It has a return tank and a gear pump with a manual handle.

## Slide 10: The Frame
Notes: The frame is the structure that everything else is built on with this project. The above frame on the left shows the structure under maximum load with very exaggerated displacement visuals. There are a few more beams to be added to the frame but we are waiting on other key parts to fabricate mounting requirements after measurements.

## Slide 11: The Frame
Minimum Safety Factor is 4
Truss Is lighter and stiffer than I beam
Notes: The frame is the structure that everything else is built on with this project. The above frame on the left shows the structure under maximum load with very exaggerated displacement visuals. There are a few more beams to be added to the frame but we are waiting on other key parts to fabricate mounting requirements after measurements.

## Slide 12
I²C 7 segment schematic
60 ohm
5 identical units will be built, and then given unique addresses

## Slide 13: Motor to Hydraulic Pump

## Slide 14: Motor Adaptor Plate

## Slide 15: Current Project Status
Frame is welded.
Piston mounting system is designed.
Load display is designed.
Software is designed.
Hydraulics are waiting on bracket to be mounted.
Frame needs more work to be ready to paint.
Load display needs to be built
Software needs to be written.

## Slide 16: Work Breakdown
Put Gaant chart screen shot here
Carter Ben
Project managed on GitHub
Notes: Here is our gaant chart with individual responsibilities and subsystems for each category. It shows due dates and what needs to be done in what order. It is available through our website via a link.

## Slide 17: Final Budget
Chart: 
| Electronics | Hydraulics | Mechanical | Raw Materials
Total | 600.95 | 1676.16 | 491.52 | 565.434
Category | Total
Electronics | $ 600.95
Hydraulics | $ 1,676.16
Mechanical | $ 491.52
Raw Materials | $ 565.43
Total | $ 3,334.06
Name | Qt | Price | Shipping | Total | 
Electronics |  |  |  |  | $ 600.95
7 segment display | 5 | $ 16.46 | $ 15.00 | $ 97.30 | 
Rasberry Pi | 1 | $ 55.00 | $ 12.72 | $ 67.72 | 
Monitor | 1 | $ 136.00 | $ - | $ 136.00 | 
hdmi cord | 1 | $ 5.79 | $ - | $ 5.79 | 
i2c ADC | 1 | $ 14.95 | $ 4.07 | $ 19.02 | 
Switches | 1 | $ 5.95 | $ - | $ 5.95 | 
Misc | 1 | $ 150.00 | $ - | $ 150.00 | 
Darlington Array | 6 | $ 2.00 | $ 4.43 | $ 16.43 | 
USB external HDD | 1 | $ 28.00 | $ 7.49 | $ 35.49 | 
7-Seg I2C | 5 | $ 5.95 | $ 7.50 | $ 37.25 | 
Wireless router | 1 | $ 30.00 | $ - | $ 30.00 | 
 |  |  |  | $ - | 
Hydraulics |  |  |  |  | $ 1,676.16
Pump | 1 | $ 171.75 | $ 24.32 | $ 196.07 | 
Motor | 1 | $ 123.00 | $ - | $ 123.00 | 
Cylinder | 1 | $ 236.50 | $ - | $ 236.50 | 
Sensor (0-5V) | 1 | $391.50 | $ - | $ 391.50 | 
Lines | 5 | $ 100.00 | $ - | $ 500.00 | 
Valve | 1 | $ 85.00 | $ - | $ 85.00 | 
Tank | 1 | $ 70.00 | $ - | $ 70.00 | 
Filter housing | 1 | $ 40.00 | $ - | $ 40.00 | 
Filter Cartridge | 1 | $ 20.00 | $ - | $ 20.00 | 
 |  |  | $ - | $ - | 
Motor Coupling | 1 | $ 4.22 | $ - | $ 4.22 | 
Pump Coupling | 1 | $ 5.29 | $ - | $ 5.29 | 
Coupling Spider | 2 | $ 2.29 | $ - | $ 4.58 | 
 |  |  | $ - | $ - | 
 |  |  |  | $ - | 
Mechanical |  |  |  |  | $ 491.52
Castors | 4 | $ 47.88 | $ - | $ 191.52 | 
Misc Hardware | 1 | $ 300.00 | $ - | $ 300.00 | 
 |  |  | $ - | $ - | 
 |  |  | $ - | $ - | 
 |  |  | $ - | $ - | 
 |  |  | $ - | $ - | 
 |  |  | $ - | $ - | 
 |  |  | $ - | $ - | 
 |  |  | $ - | $ - | 
Raw Materials |  |  |  |  | $ 315.21
Frame Steel | 0 | $ - | $ - | $ - | 
0 | .00 ft | $ 2.33 | $ - | $ - | 
0 | .00 ft | $ 3.63 | $ - | $ - | 
0 | .00 ft | $ 12.06 | $ - | $ - | 
Steel Cuts at Capitol | 6 | $ 10.00 | $ - | $ 60.00 | 
 |  | $ - | $ - | $ - | 
 |  | $ - | $ - | $ - | 
Paint | 10 | $ 7.00 | $ - | $ 70.00 | 
Aluminum plate 1'x6'x.5" | 1 | $ 185.21 | $ - | $ 185.21 | 

## Slide 18: Conclusion
In Conclusion:
  Design meets Client specs
  Design is constructible within timeframe
  Design is within budget

## Slide 19: Questions?